## Slide 1: Section 3: Remote Sensing
New technologies have changed the appearance and use of maps.
K What I Know | W What I Want to Find Out | L What I Learned

## Slide 2
Essential Questions
What are some of the different types of remote sensing?
How are satellites and sonar used to map Earth’s surface and its oceans?
What is the Global Positioning System and how does it work?
Copyright © McGraw-Hill Education
Remote Sensing

## Slide 3
Review
satellite
New
remote sensing
Landsat satellite
sonar
Global Positioning System
Geographic Information System
Copyright © McGraw-Hill Education
Vocabulary
Remote Sensing

## Slide 4
Remote Sensing
Copyright © McGraw-Hill Education
Landsat Satellite
The process of gathering data about Earth using instruments mounted on satellites, airplanes, or ships is called remote sensing.
Landsat satellites record reflected wavelengths of visible light and infrared radiation from Earth’s surface, and then computers convert the information into digital images.
Landsat data are used to study pollution, the movements of Earth’s plates, and the melting of glaciers and ice caps.

## Slide 5
Copyright © McGraw-Hill Education
Remote Sensing
OSTM/Jason-2 Satellite
One satellite that uses radar to measure and map sea surface height is the OSTM/Jason-2 satellite.
Radar uses high-frequency signals that are transmitted from the satellite to the surface of the ocean. A receiving device then picks up the returning echo as it is reflected off the water.

## Slide 6
Copyright © McGraw-Hill Education
Remote Sensing
OSTM/Jason-2 Satellite
Using OSTM/Jason-2 data, scientists are able to estimate global sea levels with an accuracy of just a few millimeters.
Scientists can use this data combined with other existing data to create maps of ocean-floor features.

## Slide 7
Copyright © McGraw-Hill Education
Remote Sensing
SeaBeam
Sonar is the use of sound waves to detect and measure objects underwater.
SeaBeam technology uses sonar to map the ocean floor from a ship.

## Slide 8
Copyright © McGraw-Hill Education
Remote Sensing
SeaBeam
A sound wave is sent from a ship toward the ocean floor. A receiving device picks up the returning echo when it bounces off the seafloor.
A computer calculates the distance from the ship to the ocean floor using the speed of sound in water and the time it takes for the sound to be reflected.
SeaBeam technology is used by fishing fleets, deep-sea drilling operations, oceanographers, volcanologists, and archaeologists.

## Slide 9
Copyright © McGraw-Hill Education
Remote Sensing
The Global Positioning System
The Global Positioning System (GPS) is a satellite navigation system that allows users to locate their approximate position on Earth.
These satellites can also relay information to a GPS receiver about elevation, direction of movement, and speed.

## Slide 10
Copyright © McGraw-Hill Education
Remote Sensing
The Global Positioning System
Uses for GPS technology
GPS technology is used extensively in navigation by airplanes and ships.
GPS receivers also help people in everyday life to find a destination or determine their current location.

## Slide 11
Copyright © McGraw-Hill Education
Remote Sensing
The Global Positioning System
Visualizing GPS Satellites
GPS receivers detect signals from the 24 GPS satellites orbiting Earth. Using signals from at least three satellites, the receiver can calculate location within 10 m.

## Slide 12
Copyright © McGraw-Hill Education
Visualizing GPS Satellites
Remote Sensing
Go to your ConnectED resources to play Animation: Visualizing GPS Satellites.

## Slide 13
Copyright © McGraw-Hill Education
The Geographic Information System
The Geographic Information System (GIS) uses a worldwide database to create layers, or “themes,” of information that can be placed one on top of the other to create a comprehensive map.
GIS map layers remain linked to the original information, so if the original information changes, the GIS layers also change. The result is a map that is always up-to-date.
Remote Sensing

## Slide 14
Copyright © McGraw-Hill Education
Review
Essential Questions
What are some of the different types of remote sensing?
How are satellites and sonar used to map Earth’s surface and its oceans?
What is the Global Positioning System and how does it work?
Vocabulary
remote sensing
Landsat satellite
sonar
Remote Sensing
Global Positioning System
Geographic Information System